## Slide 1: Asynchronous Digital Subscriber Line
ADSL

## Slide 2: What is ADSL?
It is a type of digital communication technology that enables high-speed data transmission over traditional copper telephone lines.
It is designed to provide faster data transfer rates compared to traditional analog modems, allowing for simultaneous voice and data services on the same line.
ADSL is the most widely publicized of a family of new modem technologies designed to provide high-speed digital data transmission over ordinary telephone wire.

## Slide 3: Why it is called Asymmetric?
The term "asymmetric" in ADSL refers to the fact that the upload and download speeds are not symmetrical.
ADSL technology allocates more bandwidth for downloading data from the internet than for uploading data.
This asymmetry is based on the assumption that most users typically download more data than they upload, aligning with the typical usage patterns of internet browsing, streaming, and file downloading.

## Slide 4: How does ADSL work?
In general ADSL use the following mechanisms for giving telephone and internet access on the same line.
Signal Division: The ADSL system divides the frequency spectrum of the telephone line into multiple channels. The lower frequency band is reserved for voice communication, while the higher frequency band is allocated for data transmission.
Modulation and Demodulation: At the customer end, an ADSL modem is connected to the telephone line. The modem modulates digital data into analog signals suitable for transmission over the telephone line.

## Slide 5: How does…
Upstream and Downstream Channels: ADSL is an asymmetric technology, meaning that it provides different data rates for upstream (data transmitted from the customer to the service provider) and downstream (data transmitted from the service provider to the customer).
DSL Access Multiplexer (DSLAM): At the service provider's end, the telephone lines from multiple customers are connected to a DSL Access Multiplexer (DSLAM). The DSLAM aggregates and manages the individual ADSL connections from various customers
Internet Service Provider (ISP) Network: Once the data signals reach the service provider's network, they are routed through the ISP's network to connect to the desired destinations on the internet

## Slide 6: Protocols Used in ADSL
IP-The user generates IP packets, it is necessary to transport these IP packets to the ADSL modem.
ATM- In the ADSL ,modem is decapsulating the frame to retrieve the IP packet and encapsulate it again, but this time in an ATM frame.
PPTP (point-to-point tunneling protocol), L2F (Layer 2 Forwarding) and L2TP (Layer 2 Tunneling Protocol)- These protocols allow the user authentication, dynamic address assignment, encryption of data and possibly compression.

## Slide 7: Real life applications of ADSL
Home Internet Access: ADSL is commonly used by households to access the internet. It allows users to connect multiple devices, such as computers, smartphones, and smart TVs, to the internet simultaneously
Video Streaming: ADSL provides sufficient bandwidth for streaming services such as Netflix, YouTube, and Amazon Prime Video.
Small Business Connectivity: ADSL is popular among small businesses that require reliable and reasonably fast internet access. It enables businesses to connect their computers, point-of-sale systems, and other devices to the internet